## Slide 1
TDMA Schedule Planner and Optimizer
Centralized Python scheduler using Distance-2 graph coloring
Wireless Protocol Development Internship Assignment Vaan Megam Networks
Nakul Joshi
Part 1 — Network Brain

## Slide 2
1. Problem Statement
TDMA lets radios share a frequency by transmitting in different time slots.
Direct interference
If two nearby radios communicate at the same time, they can interfere. 1-hop neighbors must use different slots.
Two-hop interference
Nodes that share a common neighbor can create a receiver collision. 2-hop nodes must also use different slots.
Spatial reuse
Nodes separated by more than two hops can reuse the same TDMA slot.
Assignment requirement: generate a conflict-free Slot × Node Boolean matrix and Node-to-Slot mapping.
VMN • TDMA Schedule Planner & Optimizer
2

## Slide 3
2. Solution Architecture
JSON
16 node coordinates
→
Graph
500 m connectivity
→
Conflict
Distance-2 graph
→
Optimize
103 colorings
→
Validate
No conflicts
→
Export
JSON + CSV
The scheduling logic is separated from CLI input/output and visualization.
VMN • TDMA Schedule Planner & Optimizer
3

## Slide 4
3. Wireless Network Graph
Graph model
• Radio → graph node • Wireless link → graph edge • Communication range → 500 m • Distance uses Euclidean geometry For every node pair: d = √((x₂−x₁)² + (y₂−y₁)²) If d ≤ 500 m, an edge is created.
Current topology
16 nodes 27 wireless links The graph is undirected and each edge stores the physical distance. This graph becomes the foundation for the Distance-2 conflict model.
VMN • TDMA Schedule Planner & Optimizer
4

## Slide 5
4. Distance-2 Conflict Graph
The wireless graph is transformed into a scheduling conflict graph.
1 hop
Directly connected radios → MUST use different slots
2 hops
Radios connected through a common neighbor → MUST use different slots
> 2 hops
No Distance-2 conflict → Slot reuse is permitted
Current topology: 53 conflict links
VMN • TDMA Schedule Planner & Optimizer
5

## Slide 6
5. Optimization Strategy
Graph coloring maps directly to TDMA scheduling:
Node
Wireless radio
Edge
Scheduling conflict
Color
TDMA time slot
Candidate strategies
• Largest-first greedy
• Smallest-last greedy
• DSATUR / saturation-largest-first
• 100 deterministic randomized greedy runs
Selection rule
Choose the valid candidate using the fewest slots. The 7-slot result is a heuristic result, not a proof of the global minimum.
VMN • TDMA Schedule Planner & Optimizer
6

## Slide 7
6. Actual Result
16
Nodes
27
Wireless links
53
Conflict links
103
Coloring candidates
7
Slots selected
Schedule validation
✓ VALID — No conflicting nodes share the same TDMA slot.
Selected heuristic: largest_first Current slot assignment:
S0: 01, 03, 11 S1: 02, 05, 07 S2: 06, 08 S3: 04, 10, 16 S4: 09, 12 S5: 14 S6: 13, 15
VMN • TDMA Schedule Planner & Optimizer
7

## Slide 8
7. Topology Visualization
VMN • TDMA Schedule Planner & Optimizer
8

## Slide 9
8. CLI, Outputs and Testing
CLI
python src/main.py --input examples/nodes.json Input validation: • Exactly 16 nodes • Two coordinates per node • Numeric coordinates Outputs: • schedule.json • schedule.csv
Testing
Pytest regression suite 9 / 9 tests passed Coverage includes: • Graph construction • Conflict generation • Schedule validation • Matrix generation • Slot assignment • Invalid node count • Invalid coordinates • Non-numeric coordinates
VMN • TDMA Schedule Planner & Optimizer
9

## Slide 10
9. EMANE Integration — Part 2 Approach
Part 2 is an integration approach, not claimed as completed functionality.
Python Optimizer
→
Schedule Matrix
→
XML / ProtoBuf Bridge
→
EMANE TDMA Radio Model
→
Virtual Radios + Packets
• Configure EMANE's native TDMA Radio Model.
• Map slot/frame/frequency concepts to the generated schedule.
• Convert the matrix into the expected schedule event format.
• Verify packet behavior in the virtual network.
VMN • TDMA Schedule Planner & Optimizer
10

## Slide 11
10. Engineering Decisions & Limitations
Why this design?
• Multiple heuristics instead of one greedy ordering • Fixed seeds for reproducibility • Explicit conflict validation • Separate modules for graph, scheduling, CLI and visualization • JSON/CSV outputs for downstream use
Current limitations
• Centralized topology knowledge • Fixed 500 m communication model • No RF/SINR/fading model in Part 1 • Seven slots is not claimed to be globally optimal • EMANE bridge is not yet implemented
VMN • TDMA Schedule Planner & Optimizer
11

## Slide 12
11. Conclusion & Next Steps
Implemented
• Centralized Python TDMA optimizer
• 500 m connectivity graph
• Distance-2 conflict graph
• Multi-heuristic slot optimization
• Conflict-free 7-slot test result
• CLI + JSON/CSV output
• Automated 9/9 tests
Next
• Finalize documentation
• Demonstrate CLI and schedule
• Explain algorithm and complexity
• Develop EMANE integration bridge
• Validate packet behavior in simulation
Thank you
VMN • TDMA Schedule Planner & Optimizer
12